| Manager/Supervisor | Lasky |  | Audit Team Leader |  |
| --- | --- | --- | --- | --- |
| Date Scheduled | 9-13-99 |  | Auditor(s): | Marc Smith |
| Date Completed: | 9-13-99 |  | Auditee(s): | Dan F |

Audit of 776 & 338 Tocco, Drill - Machines 24001 (Heat Treat), 58002, 58003 Drills

QS-9000 Elements to be Audited (refer R-17001F System Audit Matrix):

| 4.1 | Management Resp | 4.2 | Continuous Improvement | 4.5 | Document and Data Control | 4.9 | Process Control | 4.16 | Control of Quality Records |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Item # | Description | Observations/Findings/Documents Audited | Conforms ? |
| --- | --- | --- | --- |
|  |  |  | Yes | No |
| 1 |  | Review finishing machine log (Doc W-09002G 4/5/99) for 58002. Running SF-388. Logs are being completed appropriately and operator explained his role without problem. | X |  |
| 2 |  | Review drill operate and monitor check sheet rev. 6/30/96 BP change given as 8/1/97/R. Operator has completed assigned checks and annotated log. | X |  |
| 3 |  | Plug gage CB005 checked. Cal due 9/99 | X |  |
| 4 |  | Setup gage BX002 checked. Cal due 9/99 | X |  |
| 5 |  | Review filed 24001, 58002 and 58003 machine logs in file cabinet. A random sample of 10 records each revealed entries are being made as appropriate. | X |  |
| 5a |  | Reviewed filed setup check sheets. A random sample of 10 records each revealed entries are being made as appropriate. | X |  |
| 6 |  | Examined heat treat temperature controller. Calibration is about 4 months over due (due 5/99). |  | X |
| 6a |  | Operator not aware controller was a calibration item - did not recognize the calibration tag on the controller. (Training issue consistent with weak internal calibration system control as evidenced in earlier audits) |  | X |
| 7 |  | Discussed nonconforming material with auditee. He is knowledgeable of his role in the system, does his counts, knows where to take nonconforming material to ensure segregation. | X |  |
| 8 |  | Tag/sign over work bench where logs are filed reads: "Check 388 hole position - Punch mark up - Until further notice". This is dated 2-15-95 by Wes M. Should have been integrated into process documentation (4 years is a long time). |  | X |
| 9 |  | Traveler for 08172 reviewed (part SF-388) reviewed. Contents correct. | X |  |
| 10 |  | Spray bottle with unknown contents present. Operator said he doesn't know for sure what is in it for sure but thinks it is oil. |  | Observation |
| 11 |  | Process manual reviewed for contents in accordance with the index. All documents present. However, a Quality Alert dated 4-29-99 by Judy W and scheduled to be removed on 6/29/99 was still in the manual. |  |  |
| Auditee: | Date: |
| Auditor(s) | Date: |
| Quality Manager | Date: |