Guidelines for the Process Audit Approach

A - Process audit Approach:

1- Process Analysis

Process Input (What do you need?)

  - Customer requirements,

  - Production program,

  - Supplied materials,

  - Supplied parts,

  - Specifications,

  - DFMEA and PFMEA

  - Production and test equipment,

  - Trained personnel,

  - Work instruction and inspection instructions,

  - Control plan.

Process activities (What do you do?)

- Cutting, fabric

- Cutting, metal

- Sewing

- Silk screening

- Assembly

Support activities (Who helps? How?)

- Maintenance of tools and equipment/machinery,

- Logistics/transport,

- Storage,

- Packaging,

- Measuring and process analysis based on data,

- Measurement control,

- Housekeeping.

Linkages/interfaces (With who?)

- Suppliers,

- Customers,

- Production planning function,

- Engineering,

- Training,

- Human relations,

Process output

- Product delivered to the customer (Internal/External) conforming and on time.

(You may want to list the output conditions)

Measurement, for process efficiency and effectiveness and Quality

- PPM

- Delivery performance,

- Response time,

- Time for returned product test/analysis and problem solving,

- Cost of poor quality.

- Up-time/Down-time

Audit Planning (Activities for Preparation)

- Identify Process

- Analyze Process

- Risk Analysis (inputs/outputs) and Audit Priorities

- Follow up issues of prior audits (external/internal)

- Audit Plan (sequence/process steps, timing, interview partners)

- Create/complete checklist

2- Facts to be verified during the audit

- Is the process defined? Inputs, activities, outputs, monitoring, measurement, customer and product acceptance requirements.

- Have defective products been produced?

- Have defective products been segregated?

- Are there approved set-up instructions?

- Was set-up verification performed?

- Is there a reaction plan for product and process nonconformities?

- Is there evidence of corrective action

- Who maintains tooling capability?

- Do operators participate in problem analysis?

- Is product identified?

- Are there environmental procedures available?

- Is there storage and management of tools not in use.

- Additional items.

3 – Necessary information for the audit:

- Control of suspect parts in accordance with the customer requirements,

- Customer requirements on specific characteristics (visual items: method of joining, color, surface) and tolerances,

- Customer requirements on marking of EAPA’s,

- Customer requirements for packing, packaging and shipping,

- Customer requirements for part approval process

- Additional items.