# Purpose

## The purpose of this procedure is to describe requirements for evaluation and disposition of nonconforming production material to prevent unintended use or installation.

# Scope

## This procedure applies to material that has been rejected by Receiving Inspection or Work-In-Process to the Material Review Board for rapid notification and consensus regarding evaluation and disposition.

# DEFINITIONS (optional)

Material Review Board

Review panel of qualified staff that directs the handling of nonconforming materials.

MRB Location

A non-netable, non-issuable location established for holding nonconforming material until it is dispositioned.

WIP

Work-In-Process, material issued to Manufacturing or Assembly on a production work order.

RI

Receiving Inspection.

# Policy

## The MRB shall convene when necessary to disposition nonconforming material.

## The following department representatives are authorized to disposition nonconforming material for the MRB:

- Purchasing

- Manufacturing/Quality Engineering

- Manufacturing

- Design Engineering

- Planning

## Minimum 2 signatures are required to disposition nonconforming material.

## 4.3.1.	Only Purchasing signature is required for a Return to Vendor disposition when a wrong part is received.

## Any of the representatives above are authorized to call an unscheduled MRB meeting due to production need.

# PROCEDURE (See attached flowchart) (optional)

## All rejected material pending MRB disposition shall be properly identified (i.e., with MRB Tag.) and physically segregated to the designated holding area.

## The assigned MRB representatives shall disposition the nonconforming material as any of the following:

- Use as is

- Rework

- Scrap

- Return to vendor

## Quality Assurance is responsible for ensuring that MRB records are retained for 2 years minimum.

## When parts or assemblies are rejected at Receiving Inspection, an MRB tag is generated and the parts/assemblies are physically transferred to the MRB location for disposition, via a move ticket.  In the MRP system, the data entry/inventory clerk transfers the parts/assemblies from receiving inspection to MRB.

## When parts or assemblies are rejected in WIP, an MRB tag is generated by the operator or supervisor and the parts/assemblies are transferred to MRB location for disposition via a material move ticket.  In MRP system, the parts/assemblies are de-kitted from the work order  and then transferred to MRB location by the Data Entry Clerk.

## 5.5.1 Whenever possible, replacement parts/assemblies are issued to the work order.

## 5.5.2 If production is stopped due to discrepant material, MRB is immediately convened.

## Corrective Action

### For purchased material, the MRB may choose further action by way of Supplier Corrective Action Request (NPP-99060-).

### MRB may choose further action by way of an Internal Corrective Action Request per NPP-99070.

### Records are periodically reviewed for failure trends. Corrective/preventative actions is to be performed on trends identified.

### Use-as-is and Rework disposition

### A copy of the MRB tag is to go with the work order or into the stock bin.

# EXHIBITS (optional)

## MRB Procedure – Exhibit “A”

# Reference:

## MRB Tag – -FORM-038 (Example attached)

## EXHIBIT “A”

# MRB  TAG #0001

# Originator____________________  Date__________

Part #____________________  	Quantity______

Discovered in  [   ] Receiving		[   ] WIP

# PO#__________ Vendor____________ WO#_________

Discrepancy: __________________________________

______________________________________________

______________________________________________

Disposition:

[   ]RTV     [   ]Rework      [   ]Use As Is       [   ]Scrap

Follow-up: _________________________________

__________________________________________

Corrective Action Required? [   ] YES      [   ] NO

Approvals:

Manufacturing/Quality Engineer ___________________

Purchasing _____________________________________

Design Engineer or Manufacturing__________________

## EXAMPLE OF MRB Tag