MSA 4th Edition Rollout Summary 8/12/10

Presenters:  Joe Bransky –GM; Mike Down –GM; Russ Hopkins –Ford,

Patrice White-Johnson –Ford; Fred Czubak –Chrysler, Gregory Gruska –Omnex; Steve Stahley –Cummins.

A few main take-aways:

- TS Auditor relations & procedures: Bransky said, “Only PPAP is a requirement.  The other AIAG documents [APQP, MSA, PFMEA, SPC] are reference material and recommended practices but they are NOT required.”

  - He suggested that supplier procedures should make this distinction clear to avoid auditors using the whole manual as a requirement. A Lead Auditor from  Lloyds agreed with this.

  - Mike Down mentioned that “auditors…get goofy with requirements for calibrated rulers, etc.”.

  - Shop floor systems should reference ANSI/NCSLZ540.3 as well.

- Gage acceptability decision rule recommendation changed from 10/20/30 to 10, 10-30, >30.

- Stahley said, “Some GRR is not value-added. For instance, profilometer measurements are better served with the uncertainty value rather than a GRR meant to largely satisfy an auditor.”.  The Lloyds Lead Auditor agreed.

- Gruska reminded everyone that, “Calibration is a re-centering of the measurement device. If using stability as a re-calibration decision tool then re-calibration is not needed until such a time as the measurement process drifts out-of-control.

Specific Changes

- Page 73 amplifies definition of when product must span the full expected range of variation versus using the GRR parts to estimate product variation.

- The manual more clearly distinguishes between specification % used and process control limit % used.  The gage may be fine for specification decisions but insufficient for process control decisions.

- Range method replaced by σ but this is a reference manual so has little practical effect IMO.

- Capability comparison and rationale for using the 30% explained more clearly.  0-30% error has a neglible effect on Ppk/Cpk estimates.  It was noted that capability percentage uses 30% as derived from σ; when the σ² (variance) is used, the maximum is 10%.

- Risk analysis made more realistic (pg. 132/133) and the use of cross-tabulation introduced as preferred ATTRIBUTE analysis method (pg. 134-141). Opinion: it seemed well recognized by most attendees and presenters that the old attribute methods were largely ‘window-dressing’ for the customer and did not address the critical ‘grey’ decision areas at the specification limits.

- Number of Distinct Categories now truncated to the integer.  Roots of ndc minimum of 5 derived from histogram preferred cell categories which are typically 5-7.  Concensus that if variable gages are being used to make attribute decisions then this may not be an issue.

- Attribute kappa values of 1 indicate an inappropriate sample choice (Gruska) or too tight a tolerance (un-necessary product rejection).

- Observation:  We were surprised at how few tables remembered to individually number each animal cracker used in the Attribute cross-tabulation excersize.

- Amplified Destructive Testing using nested ANOVA method.

- True position recommended to use bi-variate models and MANOVA.

GENERAL HEADS-UP:  All manuals were selling for $25 USD at the training versus $75 if ordered from AIAG!

~~~~~ End of Report ~~~~~