TITLE

LASER SAFETY PROGRAM

__________________________________________________________________________________

# PURPOSE

## To protect all employees at the  Corporation site from exposure to hazardous levels of laser radiation.

## This program is also intended to ensure the  Corporation site complies with federal, state, and local regulations.

# SCOPE

## This program applies to all employees at the  Corporation site that work with or near class 2, 3, or 4 lasers.

# REFERENCE DOCUMENTS

## American National Standards Institute, Lasers Z136.1

## California Code of Regulations, Title 8, General Industrial Safety Orders, Section 3382

## Site Laser Inventory (Attachment A) and  Safety Handbook

# DEFINITIONS

## Class 1 lasers - Lasers that are not hazardous for continuous viewing or are designed in such a way that prevent human access to laser radiation. These consist of low power lasers or higher power embedded lasers (i.e. laser printers).

## Class 2 visible lasers - Lasers emitting visible light which because of normal human aversion responses, do not normally present a hazard, but could be hazardous if viewed directly for extended periods of time.

## Class 3a lasers - Lasers that normally would not cause injury to the eye if viewed momentarily but would present a hazard if viewed using an optical glass or telescope.

## Class 3b lasers - Lasers that present an eye and skin hazard if viewed directly. These lasers produce a hazardous diffuse reflection when viewed at close proximity.

## Class 4 lasers - Lasers that present an eye hazard from direct, deflected and diffuse reflections. In addition such lasers may be fire hazards and produce skin burns.

## Laser (Light Amplification by Stimulated Emission of Radiation) – An intense beam of light classified as non-ionizing radiation.

## Laser Pointer – Common tool used in presentations.  These lasers are usually class 2 or 3a.

## Laser System – An assembly of electrical, mechanical, and optical components that contains one or more lasers.

## Type – Diode

## LSO – Laser Safety Officer

# RESPONSIBILITIES

## It is the responsibility of Supervisors and Managers to:

### Inform the Operations department when new lasers are brought on site.

### Inform the Operations department when the current conditions of laser usage change.

### Ensure lasers in their department are on the site laser inventory.

### Ensure that employees follow all required procedures.

### It is the responsibility of the Operations department to:

### 5.2.1	Review and update this program.

### 5.2.2	Maintain the Site Laser Inventory (Attachment A).

### 5.2.3	Assist Managers and Supervisors with establishing safe operating procedures.

### 5.3	It is the responsibility of employees to follow this procedure when working with or around lasers.

# PROCEDURE

## General Requirements for all class 2, 3, and 4 lasers.

### Lasers must be labeled by the manufacturer with the sunburst logo.  This label states the class of the laser and must not be removed or damaged.

### The lowest class laser or laser system that effectively completes the task shall be used.

### Direct eye contact with laser beams shall be avoided at all times.

### Lasers shall never be aimed or directed towards personnel.

### Lasers shall only be used for their intended purpose based on manufacturer specifications or site operating procedures.

### Written procedures shall be developed for all alignments of lasers.

### Anodized (highly polished) tools and other reflective surfaces shall not be present while operating or aligning a laser.

## Laser Inventory

### Department managers must inform the S&H department when a manufacturer designated class 2, 3, or 4 laser is brought on site.

### Exception: Laser pointers designated by the manufacturer as class 2 or 3a do not need to be reported.

### Additional requirements exist for class 3 and 4 lasers.  The Operations department will communicate these requirements if this class of laser is brought on site.

### A site Laser Officer (LSO) will be identified and coordinate all site inspections and medical surveillance as directed by the Operations Department Manager.

### The LSO will ensure the site complies with the California Code of Regulations, Title 8, General Industrial Safety Orders, Section 3382 and any local regulations.

# TRAINING

### Employees that use lasers shall review this document upon initial assignment.

### This excludes personnel that use laser pointers.

# RECORDS AND DOCUMENTATION

### The Operations department will maintain an inventory of all lasers on site.

### Training records will be maintained in accordance with the training documentation procedures.

## ATTACHMENT A

## SITE LASER INVENTORY

| Location | Manufacturer/Model | Class |
| --- | --- | --- |
| EXAMPLES: |  |  |
| Manufacturing |  | 3B |
| Manufacturing |  | 3B |
| R & D (not in use/currently in storage) |  | 3B |
| Testing Lab |  | 3B/4 |
| Auto – Barr |  | 4 |